## Slide 1
WINDOWS SERVER ADMINISTRATION
DHCP
Reservation
How to Configure DHCP Reservation on Windows Server
Complete Technical Guide
Platform
Windows Server 2019/2022
Topic
Network Configuration

## Slide 2
PRESENTATION OVERVIEW
Contents
01
Understanding DHCP Reservation
Core concepts and fundamentals
02
Benefits & Use Cases
Why and when to use reservations
03
Reservation vs Static IP
Comparative analysis
04
Prerequisites
What you need before starting
05
Configuration Steps (GUI)
Using DHCP Manager console
06
PowerShell Configuration
Command-line automation
07
Best Practices
Expert recommendations for production environments

## Slide 3
FUNDAMENTAL CONCEPTS
What is DHCP Reservation?
DHCP Reservation is a permanent IP address assignment within a DHCP scope that maps a specific MAC address to a fixed IP address.
When a device with a reserved MAC address requests an IP, the DHCP server always assigns the same reserved address—providing pseudo-static addressing while maintaining centralized management.
MAC Binding
Each reservation binds a device's unique MAC address to a specific IP, ensuring consistent addressing.
Central Control
All reservations are managed from the DHCP server, eliminating the need to configure each device manually.
How It Works
1. Device broadcasts DHCP Discover with its MAC address
2. Server checks reservations for matching MAC
3. If match found, server offers the reserved IP
4. Device receives consistent IP every time
DHCP Reservation Flow
Client Device
MAC: 00-1A-2B-3C-4D-5E
DHCP Discover
Broadcast request
DHCP Server
Checks reservation table
Reserved IP Assigned
192.168.1.50 (fixed)

## Slide 4
KEY ADVANTAGES
Why Use DHCP Reservation?
Centralized Management
Manage all IP assignments from a single DHCP server. No need to visit each device for configuration changes—update everything centrally.
Reduced Human Error
Automated assignment eliminates typos and duplicate IP conflicts. The server ensures no two devices receive the same address.
Simplified Scalability
Adding, removing, or relocating devices becomes effortless. No manual IP tracking spreadsheets needed as your network grows.
DNS Integration
Seamlessly integrates with DNS servers for dynamic name resolution. Devices are reachable by hostname regardless of their reserved IP.
Configuration Consistency
Ensures uniform network settings across all devices. Every client receives correct gateway, DNS, and subnet mask from the server.
Easier Troubleshooting
Centralized logs and reservation tables make it simple to identify IP-related issues. No more hunting for misconfigured devices.
The Bottom Line
DHCP reservations combine the reliability of static IPs with the convenience of DHCP . You get predictable addressing without the administrative overhead of manual configuration on every device.

## Slide 5
COMPARATIVE ANALYSIS
DHCP Reservation vs Static IP
Feature | Pure DHCP | DHCP Reservation | Static IP
IP Changes Over Time | Yes | No | No
Configured On | DHCP server only | DHCP server only | Each device individually
Central Management | Yes | Yes | No
Works If DHCP Down | No (new devices) | No (new devices) | Yes
Admin Effort | Lowest | Low | Highest
Best For | Laptops, phones, guest devices | Printers, cameras, NAS, VoIP | Servers, routers, firewalls
Pure DHCP
Best for devices that frequently join and leave the network. IP addresses are dynamically assigned from the pool and may change over time.
DHCP Reservation
The sweet spot: Combines the convenience of DHCP with the stability of static IPs. Perfect for devices that need consistent addressing but don't require absolute DHCP independence.
Static IP
Essential for critical infrastructure that must remain accessible even if DHCP services fail. Requires manual configuration on each device.

## Slide 6
REAL-WORLD APPLICATIONS
Common Use Cases
Network Printers
Everyone needs to find printers at the same address. Reservations ensure consistent connectivity for all users.
No driver reconfiguration needed
VoIP Phones
Call quality policies and routing rules reference specific IPs. Reservations maintain stable voice communication.
Consistent QoS and routing
Security Cameras
NVR systems expect cameras at known addresses. Reservations facilitate easy access and management of surveillance systems.
Reliable monitoring 24/7
NAS Devices
File shares and backup jobs break if IP changes. Reservations ensure storage resources remain accessible.
Uninterrupted file access
Smart TVs & Streaming
Port forwarding and casting features depend on fixed IPs. Reservations enable seamless media streaming.
Reliable casting & AirPlay
Wireless Access Points
Management interfaces need predictable addresses. Reservations simplify AP administration and monitoring.
Easy centralized management
Decision Rule
Moves between networks? → Use DHCP. Stays on one network? → Use DHCP Reservation. Critical infrastructure? → Use Static IP.

## Slide 7
BEFORE YOU BEGIN
Prerequisites & Preparation
1
Windows Server with DHCP Role
Ensure DHCP server role is installed and configured on Windows Server 2019/2022. The server must be authorized in Active Directory.
2
Configured DHCP Scope
A valid DHCP scope must exist with available IP addresses. Define the IP range, subnet mask, gateway, and DNS servers.
3
Administrative Privileges
You need Domain Admin or DHCP Administrator permissions to create and manage reservations on the server.
Most Important: MAC Address
You must obtain the MAC address (Physical Address) of the target device before creating a reservation. This is the unique identifier that binds the device to its reserved IP.
How to Find MAC Address:
Windows: getmac /v or ipconfig /all
Linux: ip link show or ifconfig
Format: 00-1A-2B-3C-4D-5E (with hyphens) or 001A2B3C4D5E (without)
Important Consideration
Ensure the IP address you want to reserve is outside the dynamic DHCP pool range or not currently leased to another device to avoid conflicts.

## Slide 8
STEP-BY-STEP GUIDE
Configuration via DHCP Manager (GUI)
1
Open DHCP Manager
Navigate to Start → Administrative Tools → DHCP or run dhcpmgmt.msc
2
Navigate to Scope
Expand your server → IPv4 → Select your Scope → Right-click on Reservations
3
Create New Reservation
Select "New Reservation..." from the context menu to open the reservation dialog
4
Enter Reservation Details
Reservation name: Descriptive name (e.g., "Office-Printer-01")
IP address: The fixed IP to reserve (e.g., 192.168.1.50)
MAC address: Device MAC without hyphens (e.g., 001A2B3C4D5E)
Description: Optional details about the device
5
Select Supported Types
Choose DHCP only , BOOTP only , or Both . For most modern devices, select Both .
6
Add and Verify
Click Add then Close . The new reservation appears in the Reservations folder.
What is BOOTP?
BOOTP (Bootstrap Protocol) was designed to dynamically assign IP addresses when computers boot up. Unlike DHCP, BOOTP only configures TCP/IP settings during boot time, not while the OS is running.
Modern devices typically use DHCP, but selecting "Both" ensures compatibility with legacy equipment.
Force Client Renewal
After creating the reservation, the client must renew its lease to receive the reserved IP:
ipconfig /release
ipconfig /renew
Pro Tip
You can also create a reservation from an existing lease. Go to Address Leases , right-click the client, and select "Add to Reservation" .

## Slide 9
AUTOMATION & SCRIPTING
Configuration via PowerShell
Create a Single Reservation
Add-DhcpServerv4Reservation `
-ScopeId 192.168.1.0 `
-IPAddress 192.168.1.50 `
-ClientId "00-1A-2B-3C-4D-5E" `
-Name "Office-Printer-01" `
-Description "HP LaserJet - Conference Room"
View Existing Reservations
# List all reservations in a scope
Get-DhcpServerv4Reservation `
-ScopeId 192.168.1.0
# Find reservation for specific MAC
Get-DhcpServerv4Reservation `
-ScopeId 192.168.1.0 | `
Where-Object {$_.ClientId -eq "00-1A-2B-3C-4D-5E"}
Bulk Creation from CSV
Create multiple reservations at once from a CSV file:
Import-Csv -Path "C:\reservations.csv" | `
ForEach-Object {
Add-DhcpServerv4Reservation `
-ScopeId 192.168.1.0 `
-IPAddress $_.IPAddress `
-ClientId $_.MAC `
-Name $_.Name `
-Description $_.Description
}
Remove Reservations
# Remove by IP address
Remove-DhcpServerv4Reservation `
-ScopeId 192.168.1.0 `
-IPAddress 192.168.1.50
# Remove multiple at once
@("192.168.1.50", "192.168.1.51") | `
ForEach-Object {
Remove-DhcpServerv4Reservation `
-ScopeId 192.168.1.0 `
-IPAddress $_
}
Why Use PowerShell?
PowerShell enables automation, bulk operations, and repeatable deployments. Perfect for enterprise environments where you need to configure dozens or hundreds of reservations consistently. Scripts can be version-controlled and deployed across multiple DHCP servers.

## Slide 10
EXPERT RECOMMENDATIONS
Best Practices
Separate Address Ranges
Reserve a block of addresses (e.g., .1–.49) for static assignments and set your DHCP scope to start above that range (e.g., .50–.254). This eliminates overlap conflicts.
Use Reservations for Servers
Always use reservations for critical servers rather than allowing fully dynamic assignment. This ensures predictable addressing while maintaining centralized management.
Ensure High Availability
Deploy DHCP servers with failover pairs or clustering technologies. DHCP failover ensures continuous, reliable service even if the primary server fails.
Integrate with DNS
Connect DHCP with DNS for consistent name resolution. Enable dynamic DNS updates so hostnames always resolve to current IP addresses.
Document Everything
Maintain clear documentation of reservations, MAC addresses, device purposes, and locations. Use descriptive names and detailed descriptions in reservation entries.
Implement Security
Apply role-based access controls to DHCP management. Monitor for unauthorized changes and implement DHCP snooping on switches to prevent rogue servers.
Regular Auditing
Conduct periodic reviews of your DHCP reservations. Remove obsolete entries for decommissioned devices, verify MAC address accuracy, and ensure reserved IPs are still needed. Use Get-DhcpServerv4Reservation to export and review configurations regularly.

## Slide 11
Master DHCP
Reservation
DHCP reservations combine the simplicity of automatic IP assignment with the predictability of static addressing . By centralizing IP management, you reduce errors, simplify scaling, and maintain reliable network connectivity for critical devices.
Centralized
Single point of management
Reliable
Consistent IP assignments
Scalable
Grows with your network
Windows Server 2019/2022
Network Administration